PRELIMINARY SUBDIVISION PLAN CHECKLIST

PROJECT NAME__________________________________________________________

PERMIT/PROJECT #____________________________ REVIEW DATE____________

REVIEWED BY___________________________________________________________

Please address all items marked with an “X” below, as well as any additional comments on this checklist or on the redlined plans.  Please return this checklist and the redlined plans when resubmitting in order to speed up the revised plan review.

GENERAL INFORMATION:

- _____	Provide name of Developer and/or Owner with their address and telephone number(s).

- _____ 	Add note:  “All improvements to conform with Forsyth County Construction Standards

and Specifications, latest edition.”

- _____	Add note:  “Irrigation systems are prohibited on all existing and proposed County Right-

of-way and considered to be a violation of the County’s Ordinance prohibiting unpermitted right-of-way encroachments.”

- _____	Add note on all sheets:  “Notify Forsyth County Inspector 24 hours before the beginning

phase of construction.  (770) 781-2165.”

5.    _____	Add note: "Full service drives will revert to right in/right out drives if Forsyth County

determines they are creating traffic problems and/or accidents or if road is widened to a multilane highway with median."

6.    _____ 	Add note: "No structures, fences or other obstructions may be located within a drainage

or access easement without prior approval by the Forsyth County Department of Engineering."

7.    _____	Add note: "Approval of these plans does not constitute approval by Forsyth County of

any land disturbing activities within wetland areas.  It is the responsibility of the property owner to contact the appropriate regulatory agency for approval of any wetland area disturbance."

8.    _____ 	Add note: Maximum cut slopes shall be 2 horizontal to 1 vertical. Continuous fill slopes

ten (10) feet in height or less may be 2 horizontal to 1 vertical. All continuous fill slopes 				that exceed ten (10) feet in height must be 3 horizontal to 1 vertical unless: (a) a 					mechanically engineered stabilized slope is approved by the Forsyth County Director of 				Engineering; or (b) the designed and constructed slopes are certified by a registered 				engineer experienced in geotechnical engineering and licensed in the State of Georgia.

9.    _____	Provide a note stating the disposition of the property with regard to the flood plain.  State

the source (FIRM Panel Number with date of map or flood study) and show flood elevations and boundaries if applicable.

10.  _____	Existing and proposed width of right-of-way on any existing streets.  Additional right-of-

way must be deeded prior to plan approval.

11. _____	Add Note: “Approval of these plans by Forsyth County is subject to, and contingent upon the applicant obtaining any and all necessary approvals from any and all applicable agencies including, but not limited to the United States Army Corps of Engineers, the United States Environmental Protection Agency, the USDA-NRCS, Georgia Department of Natural Resources, Georgia Environmental Protection Division, and the Georgia Soil and Water Conservation Commission.

12.  _____ 	Vicinity map.

13.  _____ 	North arrow.

14.  _____ 	Seal and signature of registered professional engineer or registered land surveyor on all

sheets.

15.  _____ 	Topographic map with all elevations referenced to mean sea level and a contour interval

equal to 2 feet and all finish contours.

16.  _____ 	Graphic scale, not smaller than 1” = 100.

17.  _____ 	Benchmark used.  Show location and elevation on plans.

18.  _____ 	Origin of survey.

19.  _____ 	All boundaries with bearing and distances shown.

20.  _____ 	Provide encroachment agreement for offsite work.

21.  _____	Label all structures as either existing or proposed and provide finish floor elevation(s).

22.  _____ 	Show proposed unit or phase lines if applicable.

23.  _____	Add Note: All undisturbed buffers shall be identified with orange, four-foot tree-save fencing prior to any land disturbance (UDC Sec. 18-10.1).

24.  _____	Provide on plans a copy of the text from NPDES Permit GAR10001, GAR100002 or GAR100003 (as applicable), Part IV. EROSION, SEDIMENTATION AND POLLUTION CONTROL PLAN, Section D.3. Inspections, Subsection a. Primary Permittee, paragraphs (1) thru (5). Also provide a copy of the NOI.

25.  _____	Provide a performance bond for land disturbance activity as per Forsyth County Ordinance #73, Section V: APPLICATIONS/PERMIT PROCESS, Subsection B. Application Requirements, paragraph 7(b).  The bond amount is $3,000.00 per acre or fraction thereof of the proposed land disturbance activity. Bond approval required prior to scheduling a pre-construction meeting.

ENTRANCE(S):

26.  _____	Proposed entrance location and details must be approved by the Georgia Department of

Transportation, Gainesville District, prior to the issuance of a land disturbance permit.

27.  _____	Provide sight distance profile and sight distance certification on plan or in letter form that is specific to the project and indicates compliance with AASHTO “Policy on Geometric Design of Highway and Streets,” Chapter 9 (at-grade intersections), latest edition.  Note the posted speed limit and the actual sight distance in both directions.

28.  _____	Provide distance to nearest intersection on _____________________________________.

29.  _____	Plan view of existing County road fronting property with centerline and pavement width.

30.  _____	Provide 1” = 20’ detail of proposed entrance with existing and proposed grades, utilities,

storm drainage, and pavement specifications.

PAGE 2

31.   _____	Show location of proposed entrance monument.  Entrance monuments must be set back 10 feet (minimum) from right of way.

32.   _____           Provide decel lane typical section detail Forsyth County Standard No. 124.

33.   _____	Provide entrance and accel/decel lane striping plan Forsyth County Standard No. 125.

34.   _____	Provide ______ curbed deceleration lane from the end of radius with a _____ taper, per

Forsyth Ordinance # 101.

35.   _____	Provide minimum ______ left turn lane at proposed entrance, per Forsyth Ordinance # 101, and provide required typical section detail.

36.   _____           Final entrance design to be approved by Tim Allen, Assistant Director, Department of

Engineering, prior to construction plan sign-off.

ROADS:

37.   _____	Subdivision name and street names must be approved by Forsyth County Department of

Engineering prior to plan approval.

38.   _____	Plan and profile of all streets on a scale no smaller than 1” = 100 horizontally and 1” =

10’ vertically.

39. _____	Minimum right of way:	Collector Street				80’

Commercial Street			60’

Minor Rural Road			60’

Minor Street				50’

Cul-de-sac radius (standard)		50’

Cul-de-sac radius (oversize)		62’

40. _____	Minimum pavement width to back of curb:

Commercial Street			30’

Minor Street				24’

Cul-de-sac radius (standard)		40’

Cul-de-sac radius (oversize)		52’

Decel Lane measured from

centerline of existing road			26’

41. _____	Provide horizontal curve data.

42. _____	Minimum horizontal curve radius:	Collector Streets			300’

Minor Streets			100’

43. _____	Revise landings at road intersections to comply with Forsyth County Standard 100.

44. _____	Vertical alignment must comply with AASHTO minimum design standards (25 MPH for

residential).

45. _____             Note on all road profile sheets: “Vertical alignment complies with AASHTO minimum

Design standards for a _____ MPH road.

46. _____	Completely label all road profiles with vertical curve data, existing and proposed

elevations, stations and street intersections.

47. _____	Minimum grade on all streets of 1%.

48. _____	Maximum grades:	Collector Streets – 10%

Minor Streets 	- 14%

49. _____	Minimum radius to back of curb at intersections is 30’.

PAGE 3

50. _____	Minimum radius to right of way at interior intersections is 20’.  Provide 25’ miter at

entrance.

51. _____	Designate high back curb in all negative grade cul-de-sacs and on deceleration lane and

show limits.

52. _____	Show utilities location detail, Forsyth County Standard 110 (Std. 115 with sidewalks).

53.  _____	Show typical section detail with current paving specifications.

54. _____ 	Sign plan identifying sign location, size, and type.  Include Forsyth County Standards

171  and  172.

DRAINAGE:

55. _____ 	Submit Stormwater Management Report.

56. _____ 	Stormwater Management Report must be approved prior to scheduling a plan sign-off. Contact Renee Hoge at rphoge@forsythco.com for comments.  Schedule an appointment with Renee Hoge to review hydrology report comments.

57. _____	Acreage of all off-site drainage areas contributing to flow thru the project.

Show on plans or note if no off-site drainage.

58. _____             Provide a post-developed drainage basin area map in road construction plans.

59. _____	Plan and profile of all pipes including grade, type of pipe, 100 year HGL, elevations,

proposed cover, manholes and headwalls.

60. _____ 	Minimum of 12" of compacted fill material required over all pipes. Minimum 2.8 feet – top of pipe to top of finish pavement - required over pipes under roadway.

61. _____ 	Storm sewer slopes must be greater than or equal to 1%.

62. _____	All storm drain pipes will be a minimum of 18" in diameter.

63. _____	All storm drain pipe must be concrete under pavement within right of way.

64. _____             All storm drain pipes with > fifteen (15) feet cover shall be concrete.  > 15’ to < 20’ cover shall be Class IV.  > 20’ cover shall be Class V.

65. _____	All storm drain pipes >24” in diameter located parallel to street shall be concrete.

66. _____	100-Year upstream headwater elevation at pipes to be shown by labeling elevation and

outlining contour at that elevation.  This contour will be the drainage easement if it extends outside of the 20’ drainage easement.

67. _____	Show details for all proposed storm drainage structures per Forsyth County Standards.

68. _____	Pipe to discharge into natural draw or graded ditch with rip-rap ditch checks.  Size rip rap

aprons and provide dimensions on plans, including apron depth.

69. _____	Provide channel protection and/or permanent energy dissipation (measures in addition to rip-rap) at all outlets having a discharge velocity greater than 5 fps or a Froude Number

greater than 2.5.

70. _____	Provide complete pipe chart including pipe size, pipe gauge or class, time of

concentration, runoff coefficient, rainfall intensity, drainage area, and outlet velocity.  Design for 25-year storm.  The 100 year storm shall be used on live streams, cross drains serving 20 acres or larger, and any pipe receiving off-site drainage.

71. _____             Provide gutter spread calculations. (Maximum 8’ for 10 year storm)

PAGE 4

72. _____	Minimum 20’ storm drainage easement on all storm drain pipes, drainage swales and

water courses receiving off-site drainage.

73. _____	Minimum 20' drainage/access easement from public right-of-way required for all stormwater facilities.

74. _____	Add Note: Modular retaining wall design must be submitted to the Forsyth County Department of Engineering for approval prior to construction plan approval. Wall design must include details and specifications that are site specific and must be signed and sealed by a registered professional engineer in the State of Georgia. All walls greater than four (4) feet in height shall include a fence or handrail along the top.  ___ Provide top and bottom of wall spot elevations on grading plan.

ADDITIONAL COMMENTS: ____________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

____________________________________________________________________________________________________________________________________________________________________________

# PAGE 5